Material Safety Data Sheets U.S. Department of Labor

May be used to comply with Occupational Safety and Health Administration

OSHA’s Hazard Communication Standard. (Non-Mandatory Form)

29 CFR 1920.1200. Standard must be 		Form Approved

consulted for specific requirements 		OMB No. 1218-0072

Identity (As Used on Label and List) Note: Blank spaces are not permitted. If any item is not applicable, or information is not available, the space must be marked to indicate that.

BIOLOC SS

CAS No. 1332-09-8 , CAS# 1305-78-8

Section I

Manufacturer’s Name: Emergency Telephone Number:

Moleculoc,LLC  24 hr Assistance - CHEMTREC 800-424-9300

Address (Number, Street, City, State, and ZIP Code): Telephone Number for Information: 800-748-2048

248 State St 			Date Prepared: March 2010

Groveton, NH 03582

Section II – Hazardous Ingredients / Identity Information

Hazardous Components (Specific Chemical Identity: Common Names)

OSHA PEL ACGIH TLV

Pumice  80 mg/m3 10 mg/m3

Calcium Oxide (Lime)   C1450

Borax

Polyacrylate Polymer

%SiO2 3 mg/m3 (respirable)

Quartz, CAS No. 14808-60-7 10 mg/m3 0.05 mg/m3, respirable dust

%SiO2 + 2

Other principal, inert components: Complex silicates or oxides of Al, K, Na, Fe, Ca, Mg, Ti.

Chemical Identity, major components: Amorphous Silicon Dioxide (SiO2),Mx

Oy • SiO2 (M=Al, Ca, Mg + other minor metal oxides, with bound silica (SiO2)

Common Names: Pumice, volcanic glass, Lime, Borax, Polymer

HMIS (Hazardous Materials Identification System Ratings – NPCA/CPCA)

Based on hazard rating of 4 = Most severe

Health 0

Flammability 0

Reactivity 0

Personal Protection (suggested) Use approved dust mask; goggles to prevent eye irritation

Section III – Physical/Chemical Characteristics (N/A = Not Applicable)

Boiling Point: N/A Specific Gravity: 2.4

Vapor Pressure (mm Hg): N/A Melting Point: N/A

Vapor Density: Evaporation Rate:

(Air = 1) N/A (Butyl Acetate = 1) N/A

Solubility in Water: Negligible

Appearance and Odor: Off-white powder. No odor.

Section IV – Fire and Explosion Hazard Data

Flash Point: N/A Flammable Limits: N/A LEL: N/A UEL: N/A

Extinguishing Media: N/A

Special Fire Fighting Procedures: N/A

Unusual Fire and Explosion Hazards: None

Section V – Reactivity Data

Stability Unstable Conditions to Avoid-DO NOT USE ON HYDROFLOURIC ACIDS

Stable X No special precautions

Incompatibility (Materials to Avoid): (Reacts with acid;)

Hazardous Decomposition of Byproducts: None

Hazardous Polymerization May Occur Conditions to Avoid- ACID

Will Not Occur X 	No other hazards in the regard

Section VI – Health Hazard Data

Route(s) of Entry: Inhalation? Yes Skin? No Ingestion? Non-hazardous

Health Hazards (Acute and Chronic): Irritation of the upper respiratory tract and lungs may result from accidental or chronic occupational exposure to the dust of this product. Dust may also cause lung damage when inhaled.

CARCINOGENICITY: NTP? NO ,BioLoc SS is greater than 5 Microns,  crystalline silica IARC Monographs? Vol. 68 (1997), OSHA Regulated? No

(quartz) in respirable form In Group 1. (respriable crystalline (under 3 microns)

is classified as a carcinogen. silica inhaled in the form of quartz from occupational sources is

carcinogenic to humans.)

Signs and Symptoms of Exposure: Exposure may result in coughing, wheezing, shortness of breath, tightness in chest, irritation of the upper respiratory tract, and damage to lung tissue.

Medical Conditions Generally Aggravated by Exposure: Pre-existing asthma, bronchitis, emphysema and other lung and respiratory ailments may be aggravated by exposure to dust.

Emergency and First Aid Procedures: Material is non-poisonous. Eyes – Flush with copious amounts of cool, fresh water for 15 minutes. Inhalation – Blow nose, rinse mouth, drink water to clear throat. Remove to fresh air. If symptoms persist, see a physician promptly.

Section VII – Precautions for Safe Handling and Use

Steps to be Taken in Case Material is Released or Spilled:  Sweep up and transfer to a closed

container, or vacuum with equipment fitted with an effective filter. Transfer any broken bags to new bags without

emptying original bags.

Waste Disposal Method: Bury as non-toxic waste in an approved landfill.

Precautions to be Taken in Handling and Storing: Use techniques that minimize generating dust.

Other Precautions: Material, when wet, may be slippery on a smooth flooring. Use caution.

Respiratory Protection: We suggest use a OHSA, MSHA or NIOSH approved dust mask.

Section VIII – Control Measures

Respiratory Protection: recommend  Use an approved dust mask, such as a particulate filter respirator.

Ventilations Local Exhaust: Recommended Special, Other:

Mechanical (General):

Vacuum all spills

Use filter-equipped vacuum to remove dust;

do not blow off with compressed air.

Protective Gloves: Not Required Eye Protection: Goggles recommended but not required.

Other Protective Clothing or Equipment: Not required.

Work/Hygienic Practices: Avoid vigorous shaking of bags. Clean clothes with vacuum hose, not by blowing off.